## Slide 1: Sweeping a Terrain by Collaborative Aerial Vehicles
Alon Efrat U Arizona, USA
Mikko Nikkilä Helsinki Institute for IT
Valentin Polishchuk U Helsinki, Finland
Micha Sharir Tel-Aviv University.

## Slide 2: Typical Scenario
Child is lost in a hilly terrain
Group of searchers is formed
  walkers?
    terrain is hard to access by foot...
    slow
    manpower
  helicopters?
    expensive
    noisy
    manpower
  UAVs (Unmanned Aerial Vehicles)!
    modern flight technologies
    navigation, communication
2

## Slide 3: Challenges
Visibility is limited by terrain features
  cannot see through a mountain
Child may move to avoid being found
Need strategy to determine and synchronize UAVs motion to utilize resources efficiency:
  Elevations
  Number of UAV
  Time before re-fueling
  Quality of visibility
  Robustness visibility

## Slide 4: Related Scenarios
Search after an Alzheimer patient, escaping inmate, hostile forces, etc.
Common themes to all problems
  the person might (intentionally or accidentally) use his mobility to avoid being found
  trajectories of the UAVs should take this into account
  terrain need to be swept (to be defined formally later)
In this talk:
  Addressing the synchronized path planning problem of the UAVs,
  Understanding the underlying combinatorial structure

## Slide 5: Previous results
Our work is tangential to many previous results. A very non-conclusive list:
  Polygon Sweeping
  [Guibas et al][Efrat et al] (computational geometry, robotics)
  Opt Guards Location in terrains
  [Franklin et al] (mostly in GIS community)
  Path planning for swarms of robots
  Multiple Surveillance Cameras coordination
Experimental platform for field tests in Alps
  [Doherty et al ]
Yamaha rmax with laser and high-res camera

## Slide 6: Model: (Triangulated) Terrain
Specified by:
A triangulation of the “floor” (xy-plane) of the terrain.
  h vertex
Piecewise-linear interpolation
Triangles Sizes not uniform

## Slide 7: Efrat et al ACM GIS’12 This work prelim presented at ACM GIS 2013
Minmize total fuel consumption
  given # of guards
|g1g2| ≤ 2 grid units
  uniformly over terrain
Heuristic
High memory cost
16 x 16 grid
Top view
Min # of guards
  Feasibility
  Interesting combinatorial structure (we are not objective)
|g1g2| unrestricted
  conforms to terrain
Exact solutions

## Slide 8: Model: Curtains and Two-Sides Visibility
p
q
Given: A terrain T=T(x,y), and two positions of UAV (guards) p,q
Def: hpq, the cross section plane – plane containing p and q, and vertical to the xy-plane.
Def: The infinite slab of which is the region of hpq between the lines passing through p,q and parallel to the z-axis is the curtain Cpq
Def: Cpq is a proper curtain if every point of is seen by p or q (or both).

## Slide 9: When is edge seen (collectively by 2 guards)?
p
q

## Slide 10: Non-proper curtain

## Slide 11: Model: Feasibility of curtains
Def: Chain of guards is feasible
IFF
consecutive guards along
the chain define proper curtains.
The chain partitions the terrain into ≥ 2 portions.
The target could not move from one portion to another w/o being observed

## Slide 12: Model: Sweeping
Invariant: Area left of the chain is clean
Area right of the chain is contaminated

## Slide 13: Problem versions
UAVs capabilities:
  coordination
  path control
  altitude control
  speed control
Are guards’ tracks given?
  straight lines
  polygonal
  arbitrary
Is the number of guards given?
  Or are we minimizing it?

## Slide 14: Problem statement
Given a terrain, and a height (elevation) h above the see level
Coordinate motion of guards
So as to sweep the terrain with min number of guards.

## Slide 15: Brief explanation
Full coordination
Guards on given tracks
  each track: a segment from left to right
Arbitrary tracks:
straightforward extension
math more complex

## Slide 16: 2 guards: Main idea: Free Space Diagram (FSD)
guards positions -> a point in the (x,y)-plane
Point is yellow if the corresponding guards locations define a proper curtain.
Else point is green
Find path from LL corner to UR corner.

## Slide 17: Concatenation
Generate the FSD of guards p1p2
Generate the FSD of guards p2p3
“Glue” them – provides the coordination between 3 guards
Etc for more guards

## Slide 18: The FSP has O(n4+ε) cells (and A La Euler, same number of edges, vertices) Could be built in this time (divide and concur)
Key Theorem

## Slide 19: Implementation
60x60 grid
3 options for input terrain:
  Given terrain
  Terrain generator:
    segments -> walls -> Gaussian smoothing
  Grayscale image -> terrain
    inspired by Minecraft players :)
http://www.minecraftforum.net/topic/992750-mapping-using-real-world-terrain-data/

## Slide 20: Software
Java code to coordinate motion
MATLAB to visualize
Code is free
http://www.cs.helsinki.fi/group/compgeom/rescue.zip

## Slide 21: Output
Default terrain in our code

## Slide 22: Output
Somewhere in Arizona (~ 36.1°N 112.1°W)

## Slide 23: Output
Coordination

## Slide 24: Output
Coordination!

## Slide 25: Variant: Polygonal tracks
Free Space Diagram
guards positions -> (x,y)-plane

## Slide 26: Variant: Minimize # of guards
Arbitrary tracks -- open Are “greedy” tracks polygonal?

## Slide 27: Ingredients for the proof
Thm: The lower envelop of n functions f1(x,y),… fn(x,y) has complexity O(n2+ε)
The overlay of upper and lower envelops of n functions has complexity O(n2+ε)
In our setting, fix a terrain face f. Each terrain edge ei casts a shadow, which is a function of two variables (guards locations)
The face is properly seen if the hidden portion is not “too large” – the lower envelop is below the upper envelope.
Iteate over all pairs of edges ei, ej